## Slide 1
SMART WATER PUMP AUTOMATION SYSTEM
ESP32 + Blynk IoT | Automated 2 HP & 6 HP Pump Control
Narala Heshma Sree
B.Tech – Electrical & Electronics Engineering | SRM Institute of Science and Technology
ESP32
IoT
Protection
Automation

## Slide 2
1. Project Overview
An ESP32-based controller combining water-level sensing, current monitoring, protection and cloud supervision.
What it does
Automates and remotely monitors two water pumps: 2 HP and 6 HP.
Core controller
ESP32 DevKit V1 executes motor-control, sensor-processing and protection logic.
IoT layer
Blynk provides live status, current, runtime, mode and fault information.
Automatic and Manual operating modes
Tank and sump level supervision
Current-based over-current and dry-run protection
Maximum runtime, startup and restart delays
Remote monitoring and event notifications
2

## Slide 3
2. Objectives
Remote Control
Start/stop motors through the IoT dashboard.
Automatic Operation
Use tank and sump conditions to make motor decisions.
Protection
Detect over-current, dry-run and unsafe water-level conditions.
Monitoring
Display motor current, status, runtime and last fault.
Connected System
Maintain Wi-Fi/Blynk communication for remote supervision.
Service Flexibility
Provide controlled protection-bypass options for testing/service.
3

## Slide 4
3. System Architecture
Data flows from sensors to the ESP32, while commands and status are exchanged through Blynk Cloud.
Blynk Cloud / App
ESP32 DevKit V1
Tank / Sump Float Inputs
SCT Current Sensors
Relay / Contactor Interface
2 HP / 6 HP Water Pumps
Wi-Fi / Blynk communication
4

## Slide 5
4. Hardware & Software Stack
Hardware
• ESP32 DevKit V1 • SCT current sensors ×2 • Float switches ×4 • Relay interface • Motor contactors • Wi-Fi router • 2 HP & 6 HP pumps • Isolated low-voltage control supply
Software / Firmware
• Arduino IDE • Embedded C++ • ESP32 Arduino core • Blynk IoT • EmonLib for RMS current calculation • BlynkTimer for periodic tasks • Virtual pins for dashboard control/status
5

## Slide 6
5. Motor Automation Logic
2 HP Pump — Automatic Mode
Tank LOW ↓ Start 2 HP ↓ Monitor current & protection ↓ Tank FULL → Stop Additional trips: • Over Current • Dry Run Current • Sump Dry • Maximum Runtime
6 HP Pump — Automatic Mode
Sump DRY + Sump not FULL ↓ Start 6 HP ↓ Monitor current & protection ↓ Sump FULL → Stop Additional trips: • Over Current • Dry Run Current • Maximum Runtime
6

## Slide 7
6. Protection & Timing
Configured firmware values — to be verified against the actual motor, sensor calibration and protection requirements before field deployment.
Over-current limit
13.0 A
2 HP / 6 HP
Dry-run threshold
1.0 A
Current based
Startup protection delay
10 s
Protection inhibited during startup
Over-current confirmation
3 s
Condition must persist
Dry-run confirmation
10 s
Condition must persist
Restart delay
5 s
Prevents immediate restart
Normal maximum runtime
15 min
Compile-time setting
Test-mode maximum runtime
50 s
Controlled bench testing
7

## Slide 8
7. Current Monitoring & Signal Processing
Sensing
SCT current sensors are connected to ESP32 input-only ADC pins: GPIO 34 → 2 HP current GPIO 35 → 6 HP current
Processing
EmonLib calculates RMS current. The firmware then applies: • Low-level noise suppression • Low-pass filtering • Threshold comparison • Time confirmation before trip
Dashboard
Live current values are sent to Blynk. The dashboard can display: • 2 HP current • 6 HP current • Motor status • Last fault/status
8

## Slide 9
8. Hardware Implementation & Prototype
Actual motor control panel and ESP32 prototype used for the project
Prototype Hardware
• ESP32-based control electronics
• Motor contactor and control interface
• Current-sensing CT/SCT interface
• Low-voltage relay/control wiring
• Three-phase motor connection section
• Prototype wiring used for functional testing
The ESP32/relay section is used as the control layer; motor power circuits require correctly rated contactors, overload/short-circuit protection, isolation and proper earthing.

## Slide 10
8. Blynk IoT Dashboard
Actual project dashboard screenshots
10

## Slide 11
9. Dashboard Functions Visible in the Prototype
AUTO / MANUAL
Operating mode selection and indication.
2 HP / 6 HP CONTROL
Separate motor start/stop controls and running indicators.
CURRENT
Live current gauges for both motors.
TANK / SUMP STATUS
Level-condition indicators for automation decisions.
RUNTIME
Motor runtime tracking in minutes.
FAULT / STATUS
Last fault/status and protection-related information.
BYPASS CONTROLS
Float, over-current and dry-run bypass for controlled service/testing.
CLOUD MONITORING
Blynk-based remote dashboard and event notifications.
11

## Slide 12
10. Implementation & Demonstrated Result
ESP32 firmware integrates motor control, water-level sensing, current measurement and protection logic.
Blynk dashboard provides a single interface for control and real-time status.
The project supports both automatic and manual operation.
The firmware records motor runtime and maintains a last-fault/status indication.
Current sensing uses RMS calculation with filtering to reduce low-level noise.
The repository is structured for documentation, source code, hardware details and future development.
2 HP
Pump control
6 HP
Pump control
4
Float inputs
2
SCT inputs
Blynk
Cloud dashboard
12

## Slide 13
11. Future Scope & Developer Profile
Future Development
• Energy measurement • Power factor monitoring • Flow sensor integration • Water consumption logging • Dedicated web dashboard • MQTT support • OTA firmware updates • GSM/4G backup communication • Historical cloud data • Advanced alarm management • Improved PCB protection and isolation
Developer
Narala Heshma Sree B.Tech – Electrical & Electronics Engineering SRM Institute of Science and Technology Skills demonstrated: • Embedded C++ • ESP32 • IoT / Blynk • Electrical automation • Motor protection • Sensor interfacing • Relay control • Industrial control concepts
13

## Slide 14
12. GitHub Project Repository
The project is documented and organized as a complete engineering repository.
Repository Contents
• README.md
• ESP32 firmware (.ino)
• Hardware wiring documentation
• Blynk virtual-pin documentation
• Test plan
• Required libraries
• Changelog & contribution files
• MIT License
GitHub repository: Smart_Motor_WaterPump_Automation

## Slide 15
PROJECT PORTFOLIO
Smart Water Pump Automation System
ESP32 • Embedded C++ • Blynk IoT • Motor Protection • Automation
README.md
Project explanation
Source Code
ESP32 / Arduino firmware
Images
Hardware & dashboard evidence
PPT / PDF
Interview-ready presentation
Educational / engineering-development project. Final field installation requires correctly rated protection, isolation and professional electrical design.