## Slide 1
SMART WATER PUMP AUTOMATION SYSTEM
ESP32 + Blynk IoT
Automated 2 HP & 6 HP Pump Control • Monitoring • Protection
ESP32
IoT
Automation
Protection
SC Monitoring
Narala Heshma Sree
B.Tech – Electrical & Electronics Engineering | SRM Institute of Science and Technology
SENSE
PROCESS
PROTECT
CONTROL

## Slide 2
01 | PROJECT OVERVIEW
From sensor inputs to cloud-based motor supervision.
SMART CONTROL
Automates and remotely monitors 2 HP and 6 HP water pumps.
ESP32 CORE
Executes motor-control, sensing, timing and protection logic.
BLYNK IoT
Provides live status, current, runtime, mode and fault information.
SENSORS
ESP32
PROTECTION
RELAYS
MOTORS
CLOUD
• Automatic / Manual operation
• Tank and sump level supervision
• Current-based over-current and dry-run protection
• Runtime, startup and restart management
• Remote monitoring and event notifications
2

## Slide 3
02 | PROJECT OBJECTIVES
Engineering goals addressed by the prototype.
REMOTE CONTROL
Start/stop motors through the IoT dashboard.
AUTO OPERATION
Use tank and sump conditions for motor decisions.
PROTECTION
Detect over-current, dry-run and unsafe conditions.
MONITORING
Display current, status, runtime and last fault.
CONNECTED SYSTEM
Maintain Wi-Fi/Blynk communication.
SERVICE FLEXIBILITY
Controlled bypass options for testing/service.
3

## Slide 4
03 | SYSTEM ARCHITECTURE
A connected control loop between sensors, ESP32, protection and the Blynk cloud.
ESP32 DEVKIT V1
BLYNK CLOUD / APP
TANK / SUMP FLOATS
SCT CURRENT SENSORS
RELAY / CONTACTOR
2 HP + 6 HP PUMPS
Wi-Fi / IoT
4

## Slide 5
04 | HARDWARE & SOFTWARE
Technology stack used in the prototype.
HARDWARE
ESP32 DevKit V1 SCT current sensors ×2 Float switches ×4 Relay interface Motor contactors Wi-Fi router 2 HP & 6 HP pumps Isolated low-voltage control supply
SOFTWARE / FIRMWARE
Arduino IDE Embedded C++ ESP32 Arduino core Blynk IoT EmonLib for RMS current BlynkTimer Virtual pins for dashboard control/status
5

## Slide 6
05 | MOTOR AUTOMATION LOGIC
Automatic operating sequence for both pumps.
2 HP PUMP — AUTO
TANK LOW ↓ START 2 HP ↓ MONITOR CURRENT + PROTECTION ↓ TANK FULL ↓ STOP Trips: Over Current • Dry Run • Sump Dry • Maximum Runtime
6 HP PUMP — AUTO
SUMP DRY + NOT FULL ↓ START 6 HP ↓ MONITOR CURRENT + PROTECTION ↓ SUMP FULL ↓ STOP Trips: Over Current • Dry Run • Maximum Runtime
6

## Slide 7
06 | PROTECTION & TIMING
Configured firmware values — verify against actual motor, sensor calibration and field protection requirements.
OVER-CURRENT
13.0 A | Configured threshold
DRY-RUN
1.0 A | Current-based detection
STARTUP DELAY
10 s | Protection delay after start
OC CONFIRMATION
3 s | Condition must persist
DRY-RUN CONFIRMATION
10 s | Condition must persist
RESTART DELAY
5 s | Prevents immediate restart
NORMAL MAX RUNTIME
15 min | Normal firmware setting
TEST MAX RUNTIME
50 s | Controlled bench testing
7

## Slide 8
07 | CURRENT MONITORING
RMS current measurement with filtering and protection confirmation.
SENSING
GPIO 34 → 2 HP current GPIO 35 → 6 HP current SCT current sensors feed ESP32 ADC inputs.
PROCESSING
EmonLib RMS calculation ↓ Noise suppression ↓ Low-pass filtering ↓ Threshold comparison ↓ Time confirmation
DASHBOARD
Live current values Motor status Runtime Last fault/status All presented through the Blynk IoT interface.
8

## Slide 9
08 | HARDWARE IMPLEMENTATION
Actual motor control panel and ESP32 prototype.
MOTOR CONTROL PANEL
Three-phase motor/control section, contactor, control wiring and supply section.
ESP32 PROTOTYPE
Low-voltage relay/control wiring and current-sensing interface used for functional testing.
REAL HARDWARE
FUNCTIONAL TEST
9

## Slide 10
09 | BLYNK IoT DASHBOARD
Actual project dashboard screenshots.
Dashboard — upper controls
Dashboard — monitoring
10

## Slide 11
10 | DASHBOARD FUNCTIONS & RESULT
What the working prototype demonstrates.
AUTO / MANUAL
Operating mode selection
2 HP / 6 HP
Separate start/stop control
CURRENT
Live current gauges
TANK / SUMP
Level-condition indication
RUNTIME
Motor runtime tracking
FAULT / STATUS
Last fault/status information
BYPASS
Controlled service bypasses
CLOUD
Blynk event monitoring
11

## Slide 12
11 | DEVELOPER & GITHUB
Project documentation and portfolio readiness.
DEVELOPER
Narala Heshma Sree B.Tech – Electrical & Electronics Engineering SRM Institute of Science and Technology Embedded C++ ESP32 IoT / Blynk Electrical automation Motor protection Sensor interfacing Relay control
GITHUB REPOSITORY
12

## Slide 13
12 | FUTURE SCOPE
NEXT DEVELOPMENT
Energy measurement • Power factor monitoring • Flow sensor integration Water consumption logging • Dedicated web dashboard • MQTT OTA firmware updates • GSM/4G backup • Historical cloud data Advanced alarm management • Improved PCB protection and isolation
PROJECT PORTFOLIO
Smart Water Pump Automation System
ESP32 • Embedded C++ • Blynk IoT • Protection • Automation
ESP32
IoT
Protection
Automation
Educational / engineering-development project. Final field installation requires correctly rated protection, isolation and professional electrical design.
13